## Slide 1: Water Resources Management
Lecture 2 – engineering ECONOMY

## Slide 2: Engineering Economy
Application of economics principles to assign value to an alternative
Decision principles used to select the best alternative based on value

## Slide 3: determining ECONOMIC VALUES
Economic value – a basis for comparisons
Definitions/Concepts
Economic Analysis
  Principles of engineering economics
  Cash flows
  Discounting methods

## Slide 4: determining ECONOMIC VALUES
Economic value – a basis for comparisons
Values appear at different times in an alternative
Values appear as different kinds in an alternative

## Slide 5: Equivalence of kind
Consider two designs; same cost to build (in monetary terms)
  Project 1 produces x tons of peaches
  Project 2 produces y bales of cotton
Tons of peaches and bales of cotton are not directly comparable – they are different “kinds” of outputs.
  Could use some kind of conversion rate: y’ tons peaches = y bales of cotton
  Kind of a nuisance, usually use monetary units; 1 ton peaches = X dollars 1 bale cotton = Y dollars

## Slide 6: Equivalence of TIME
Consider two designs; same cost to build (in monetary terms)
  Project 1 produces x tons of peaches
  Project 2 produces y bales of cotton
When are the peaches available? How about the cotton?
  X dollars today, or X dollars in 5 years? Which is more valuable today?
Comparisons need to account for arrival times of the benefits (and costs)
Usually use cash-flow concepts and monetary discounting
Notes: Use cash-flow to compare alternatives using monetary units recoverable at some common point in time. Monetary discounting is important as it effects the type of alternative that will appear preferable. Read (pg 5 James and Lee)

## Slide 7: Who benefits
Viewpoints (for decision making)
  The project sponsor
  The project community (who uses the outputs and derive indirect benefit)
  The entire “nation”
Notes: Pg 5 james and lee – read the relevant portion

## Slide 8: Sunk costs
Should compare alternatives on their value only – disregard history unless affect future cash flow.
Sunk costs are expenses already used; are not recoverable.
  ”Don’t throw good money after bad …”
Notes: Pg 5 7 James and lee

## Slide 9: incremental costs
Decision to add cost to a project is defendable if the incremental benefit increase exceeds the incremental cost
Notes: Pg 5 7 James and lee

## Slide 10: intangible
Some things are really hard to assign a monetary value
These are called intangible or irreducible
Surrogate values can be assigned by policy
  Human lives have a policy assigned monetary value:
    The New York Times reports that the Environmental Protection Agency values human life at $9.1 million.
    In 2008, the FDA valued human life at $5 million, today their figure sits at $7.9 million.
    State of Texas valued human life at $250,000 (Tort value cap)
Notes: Pg 5 7 James and lee
http://www.gilmanbedigian.com/tort-reform-and-the-value-of-human-life

## Slide 11: uncertainty
Comparing alternatives usually has to look into the future – inherent uncertainty
  Uncertain objectives
  Uncertain constraints
  Uncertain public response
  Uncertain technological change
  Uncertainty in recurring events (e.g. flooding magnitude and times)
Notes: Pg 5 7 James and lee

## Slide 12: Planning horizon
Design life (economic)
  Typically 50 to 100 years
Service life (physical life)
  Variable – technology can change, need can change, the thing can break
Compare things over the same period of analysis – using negative (salvage) cash flow if necessary to use comparable planning horizons

## Slide 13: Alternative structure (for comparisons)
Alternatives capable of achieving the design objective should be defined
Identify consequences of each alternative and express in monetary units
Comparisons should be on cost-to-go (to eliminate consideration of sunk costs)
Intangibles should be identified – search policy to see if economic values are already assigned (or surrogates are available)
Compare on uniform basis over common analysis periods